## Slide 1: Sensoris
사용법
좌표체계

## Slide 2: Sensoris의 설계 사상
기준점으로 상대거리를 절대좌표로 변환해 센서가 관측한 대상의 위치를 기술하는 것은 Sensoris의 좌표체계의 핵심적인 기능
  정밀한 절대좌표로 변환하는 것이 Sensoris 좌표체계의 목표
Sensor로 관측되는 대상의 위치와 정보를 외부 서버, 다른 차량과 공유
  Sensoris의 좌표체계로 정밀한 절대좌표로 변환가능

## Slide 3: Sensoris의 차량 좌표 시스템 기준점
In SENSORIS the vehicle reference point is located by convention in the middle of the rear axis.(ISO 8855:20112)
SENSORIS vehicle coordinate system

## Slide 4: origin.position_and_accuracy
SENSORIS vehicle coordinate system
Sensor(GNSS)
Event_group
metric_event_group.y
metric_event_group.x
Wgs84|ECEF grid system
metric_vehicle.x
metric_vehicle.y
Vehicle_ Front
Vehicle_ Rear
Wgs84|ECEF North
Vehicle_ Right
Wgs84|ECEF East
Vehicle_ Left
data_message_.event_group.origin
position_and_accuracy
geographic_wgs84
metric_vehicle
metric_event_group
metric_ecef

## Slide 5: origin.position_and_accuracy
geographic_wgs84
  Geographic position in World Geodetic System 84 (WGS84) reference system.
metric_vehicle
  Metric position in SENSORIS vehicle coordinate system.
  이 값과 SENSORIS vehicle coordinate system의 좌표값으로 geographic_wgs84, metric_ecef 계산가능
metric_event_group
  Metric position in relative coordinate system, the reference coordinate system is the origin of the event group.
  event_group에서만 사용하는 기준점이 필요할 때 사용.(옵션)
metric_ecef
  Metric position in Earth-Centered Earth-Fixed (ECEF) reference system.
  GSNN Raw Fix를 그대로 쓰거나, geographic_wgs84을 ECEF로 변환해 사용

## Slide 6: origin.orientation_and_accuracy
Quaternion은 yaw, pitch, roll의 축회전 후 바뀐 xyz축의 값을 dx, dy, dz으로, w는 전체 회전량을 나타냄
그림 출처: https://kr.mathworks.com/help/uav/ref/quaternion.rotateframe.html

## Slide 7: mounting_position_and_orientation.translation_and_accuracy
Wgs84|ECEF grid system
SENSORIS vehicle coordinate system
ORIGIN_Position
metric_vehicle.y
metric_vehicle.x
Vehicle_ Front
Vehicle_ Rear
Wgs84|ECEF North
Vehicle_ Right
Vehicle_ Left
Wgs84|ECEF East
Wgs84|ECEF.x
metric_vehicle.x
Mounted Sensor
Wgs84|ECEF.y
metric_vehicle.y
RED:ORIGIN
GREEN:SENSOR

## Slide 8: RectangularBoxAndAccuracy.center_orientation_size
Wgs84|ECEF grid system
ORIGIN_Position
metric_vehicle.x
metric_vehicle.y
Vehicle_ Front
Vehicle_ Rear
Wgs84|ECEF North
Vehicle_ Right
Vehicle_ Left
Wgs84|ECEF East
Wgs84|ECEF.x
metric_vehicle.x
Mounted Sensor
Wgs84|ECEF.y
metric_vehicle.x
metric_vehicle.y
geographic_wgs84.y
RED:ORIGIN
GREEN:SENSOR
Static
Object
Half-width
Half-length
metric_vehicle.x
geographic_wgs84.x

## Slide 9: RectangularBoxAndAccuracy.center_orientation_size
Wgs84|ECEF grid system
ORIGIN_Position
metric_vehicle.x
metric_vehicle.y
Vehicle_ Front
Vehicle_ Rear
Wgs84|ECEF North
Vehicle_ Right
Vehicle_ Left
Wgs84|ECEF East
Wgs84|ECEF.x
metric_vehicle.x
Mounted Sensor
Wgs84|ECEF.y
metric_vehicle.x
metric_vehicle.y
geographic_wgs84.y
RED:ORIGIN
GREEN:SENSOR
Static
Object
Half-width
Half-length
metric_vehicle.x
geographic_wgs84.x

## Slide 10: RectangularBoxAndAccuracy.corner_vectors 직사각형 형상 구현 예시
x
y
-z
0
dx
dz
dy
x
y
-z
0
2dy
2dz
2dx
2dy
2dz
2dx
x
y
-z
0

## Slide 11: RectangularBoxAndAccuracy. corner_vectors
Wgs84|ECEF grid system
ORIGIN_Position
metric_vehicle.x
metric_vehicle.y
Vehicle_ Front
Vehicle_ Rear
Wgs84|ECEF North
Vehicle_ Right
Vehicle_ Left
Wgs84|ECEF East
Wgs84|ECEF.x
metric_vehicle.x
Mounted Sensor
Wgs84|ECEF.y
metric_vehicle.x
RED:ORIGIN
GREEN:SENSOR
Static
Object
CornerVector_1
CornerVector_2
CornerVector_3

## Slide 12: RectangularBoxAndAccuracy.corner_vectors 센서관측 벡터 변환(기준점:origin, first_and_accuracy)
Static
Object
ORIGIN_Position
CornerVector_1->First Vector
CornerVector_2->Second Vector
CornerVector_2->Third Vector
first_and_accuracy.metric_origin.y
first_and_accuracy.metric_origin.x

## Slide 13: RectangularBoxAndAccuracy.corner_vectors 직사각형 형상 구현 예시
x
y
-z
0
x
y
-z
0
x
y
-z
0

## Slide 14: 차량 좌표 시스템
Sensoris의 사상대로 좌표시스템을 구현하려면 아래 두 값이 반드시 필요
  하나의 센서의 절대좌표값(x, y, z)
  그 센서의 SENSORIS vehicle coordinate system와의 Offset 값(dx, dy, dz)
이 정보를 가장 쉽게 얻을 수 있는 센서는 GNSS로 Sensoris에는 GNSS 센서로서의 정보가 아닌 직접적인 필드가 없으므로 아래와 같은 방식을 제안할 수 있다.
  sensoris.protobuf.categories.localization.VehiclePositionAndOrientation 필드에 차량의 위치 정보를 GNSS 수신 위치 정보를 넣으면
  GNSS 센서의 SENSORIS vehicle coordinate system과의 상대값으로 정의 된 설치 위치를 통해
    SENSORIS vehicle coordinate system의 절대 위치를 계산
  SENSORIS vehicle coordinate system를 통해 Sensoris의 모든 필드의 상대위치를 절대 위치로 변환 가능

## Slide 15: 차량 좌표 시스템 구현 예시
Wgs84|ECEF grid system
ORIGIN_Position
metric_vehicle.x
metric_vehicle.y
Vehicle_ Front
Vehicle_ Rear
Wgs84|ECEF North
Vehicle_ Right
Vehicle_ Left
Wgs84|ECEF East
Wgs84|ECEF.x
metric_vehicle.x
Mounted Sensor
Wgs84|ECEF.y
metric_vehicle.x
RED:ORIGIN
GREEN:SENSOR
Static
Object
CornerVector_1
CornerVector_2
CornerVector_3